## Slide 1: Getting Started with JT65 and JT9 on the HF Bands
By John Bartos, AB3LZ

## Slide 2: What is JT65?
A form of digital communications originally developed by Joe Taylor, K1JT, for Moon-bounce (EME) applications where signals are extremely weak (VHF/UHF).
Uses sophisticated digital signal processing
Also relies on redundancy – it sends the information over and over

## Slide 3: Who is Joe Taylor (K1JT)
Licensed as a teenager (K2IPT).
A math wiz whose interest in radios led to a career in radio astronomy.
Co-discoverer of the first pulsar in a binary system.
Tracked shrinking orbit of this binary system for 30 years.
Orbit was shrinking due to mass transfers.

## Slide 4: Who is Joe Taylor (K1JT)
Proved the orbit shrinking and mass loss was due to gravitational radiation.
Predicted by Einstein's Theory of General Relativity to an accuracy of 1%.
First to prove the existence of gravitational radiation.
Awarded the Noble Prize in physics in 1993.
Retired physicist/professor but still an active ham working on weak signal recognition.

## Slide 5: 65 Different Tones
A 1270.5 Hz synchronizing tone
64 additional tones to carry the information (FSK)
On the air it sounds like someone playing music

## Slide 6: Timing is Everything
Each JT65 transmission lasts precisely 46.8 seconds.
During transmission only a small amount of information is sent – about 13 characters
Station clocks must agree within about 1 seconds (Accurate time is important)
As much as 80% of the transmission can be lost and still be decoded

## Slide 7: Taking Turns
Stations take turns transmitting
Stations transmit on even or odd UTC minutes, and then listen on the following minutes

## Slide 8: Just the Facts!
A JT65 contact is designed to exchange the bare minimum information needed to qualify as a “QSO”
Call signs
Signal Reports
Grid Squares

## Slide 9: Transmitting and Receiving by Turns – Typical QSO

## Slide 10: WSJT (Weak Signal Joe Taylor)
Program written by K1JT to facilitate weak signal VHF/UHF communications.
Supported 4 communication protocols:
  FSK441: for meteor scatter
  JT6M: for ionospheric scatter
  JT-65: for EME at VHF/UHF and for HF skywave propagation
  JT4: For EME and tropospheric propagation on microwave bands
Not user friendly.

## Slide 11: JT65 on HF
The JT65 “revolution” on the HF bands is primarily due to Joe Large, W6CQZ.
Joe wrote a piece of software called JT65-HF that makes it much easier to operate JT65 and make successful contacts.
JT65-HF is currently available for Windows only.
Excellent mode for low power or antenna restricted stations.

## Slide 12: WSJT-X
Joe Taylor wrote user friendly software adapting the original VHF/UHF program (WSJT) to HF operation.
Joe has also developed WSJT-X which decodes both JT-65 and JT-9.
Programs available for Windows and MAC OS.
Source code is available to compile on LINUX operating systems.

## Slide 13: JT9 on HF, MF and LF
JT9 is a new weak signal protocol for HF, MF and LF use.
Functionally similar to JT65
Differences:
  9 tones in lieu of 65.
  BW of 15.6 HZ in lieu of ~185 HZ.
  JT65 decoder clamped at -1dB and JT9 decoder good to +49dB. (JT9 decoder linear over a large range)
  JT65 S/N threshold is -25dB vs. the JT9 threshold @ -27dB.
Software operation identical for both modes.

## Slide 14: Contacts by the “Colors”
WSJT-X uses color highlighting to indicate which stations are calling CQ, which stations are in contact with each other, and which stations are transmitting to you.
The program also has preformatted responses that you can send by simply double clicking on the appropriate line.

## Slide 15
WSJT-X Control Panel

## Slide 16: WSJT-X Water Fall Plots
JT-65 Water Fall & FFT

## Slide 17: WSJT-X Water Fall Plots
JT-9 Water Fall & FFT

## Slide 18: Let’s Follow an Actual Contact, Step by Step
I made this contact while running just 15W on 20 meters using 24 ft. vertical wire running up my chimney.

## Slide 19: I’m Calling CQ…

## Slide 20: KD6GHX Has Answered. I’m Replying with a Signal Report

## Slide 21: KD6GHX Confirms My Report and Gives Me a Report of -05 dB. I Reply “RRR”

## Slide 22: KD6GHX Sends 73 and I do the Same

## Slide 23: You Can Also Send Short Text Messages. The White Text is W4HM Telling Me that he is Running 4W to a Loop Antenna

## Slide 24: WSJT-X is Bilingual

## Slide 25: WSJT-X is Bilingual

## Slide 26: Understanding the WSJT-X Decoding Screen
UTC – When the signal was received.
dB - The strength (S/N) of the received signal in dB. Higher is better. -1 is the upper limit.
DT – The calculated offset of the received signal from your local clock. Values of .3 to 1.9 are typical.
Freq – Offset in Hz from the center point (0).
# @ – # is a JT65 decode and @ is a JT9 decode.
Message – Information exchange.

## Slide 27: JT65 & JT9 Contacts Are Valid For Most Awards
DXCC
Worked All States
Worked All Continents
eQSL Awards
Also supported by ARRL’s Logbook of The World

## Slide 28: What Do You Need to Try JT65 on HF?
SSB Transceiver
Computer with sound device
Interface

## Slide 29: Download and Install the Free JT65 Software
WSJT-x
  http://www.physics.princeton.edu/pulsar/K1JT/wsjt.html
  http://www.physics.princeton.edu/pulsar/K1JT/WSJT-X_Users_Guide_v1.1.pdf
  http://obriensweb.com/wsjtx.html (The Old Codger’s Guide to JT65 and JT9 via WSJT-X Software)
JT65-HF
  http://jt65-hf/downloads/
Clock Programs (Time is Important)
  http://www.satsignal.eu/ntp/setup.html (Meinberg NTP)
  http://www.thinkman.com/dimension4/

## Slide 30: Configure the Software First

## Slide 31: Configure the Software First

## Slide 32: Define Tx Macros

## Slide 33: Define Default Frequecies

## Slide 34: If you have an Internet Connection, You can Participate in the Reporting Network
http://pskreporter.info/pskmap.html

## Slide 35: I Monitored Reception of my JT65 15W Signal on PSKReporter

## Slide 36: I Monitored Reception of my JT9 15W Signal on PSKReporter

## Slide 37: Stations I Monitored and Reported to pskreporter

## Slide 38: db Refresher
% Power = 100% X anti log (db/10)
% Voltage = 100% X anti log (db/20)
S/N Ratio with respect to power received:
  0 db = 100% (signal power =100% of noise power)
  -5 db = 31.6% (signal power =31.6% of noise power)
  -10 db = 10% (signal power =10% of noise power)
  -15 db = 3.1% (signal power =3.1% of noise power)
  - 20 db = 1.0% (signal power =1.0% of noise power)
  -25 db = 0.32% (signal power =0.32% of noise power)
  -27 db = 0.2% (signal power =0.2% of noise power)

## Slide 39: See You on JT65 and JT9!
Questions and Comments